## Slide 1: Requirements, Functional, Logical, Physical (RFLP)

## Slide 2
Document Requirements
Create Functional Architecture
Create Logical Architecture
Specifications
Include EID
Implementing a Change
MID/
Process Plan
EID Structure/
CAD Model
RFLP
Collaboration Tasks
Requirements
Functional & Logical Design

## Slide 3: RFLP Overview
RFLP is a collaborative engineering methodology that enables requirements for a customer’s product to be captured, managed, and tracked in a single point of access, allowing for full traceability.
It allows data to be shared across the specific discipline, allowing for better traceability and change impact analysis on the entire system.
RFLP enables individuals or teams responsible for the overall design of an end-product to have visibility on the subcomponents that make up the entire system.
The concept of RFLP is tied back to processes defined in the Systems Engineering discipline.
REQUIREMENTS
FUNCTIONAL
LOGICAL
PHYSICAL
Traceability is the ability to identify the relationship between different stages of the development process of a product’s feature.
R
F
L
P

## Slide 4: What Is RFLP
RFLP is a Systems Engineering process that uses a structured approach to integrate all disciplines in moving from NEEDS to PRODUCT.
Representative of the Architecture Definition and Decomposition Curve of the V model.
Data shared across the specific discipline, allowing for better traceability, visibility and change impact analysis on the entire system.
Needs
Product
(Virtual or Real)
Systems Engineering
Validation & Qualification
Verification
Integration
Solution
Requirements Management
Functional Analysis
Logical Architecture Definition
Physical
R
F
L
P

## Slide 5: RFLP Definitions
Each segment of the RFLP process represents different types of data necessary to define the product.
  Requirements = Describes the customer’s requirements
  Functional = Describes what the system does (functionality)
  Logical = Describes what the system is (equipment, parts, interfaces)
  Physical = Describes a solution of the system (virtual or real link to the business activity)
Consider an example of how a calculator design can be broken down:
System shall
have numbers
R
F
a
b
Function
Y=a+b
Y
L
Keyboard
Display
Processor
Memory
P
Add Numbers
R
Get Numbers
Memorize
Display Result
Make Addition
…
F
Processor
Memory Chip
Screen
L
Memory Card
LCD Flat Screen
Calculator Housing
P
Functional Breakdown Structure
Logical Breakdown Structure
Logical Breakdown Structure
Number Pad
Number Pad
PN1031
PN1032
PN1021
PN102
PN103
PN100

## Slide 6: RFLP in the 3DEXPERIENCE Platform
Within the 3DEXPERIENCE Platform, the RFLP process is tracked and managed in two applications:
  ENOVIA Traceable Requirement Management (TRM)
    Create and manage requirements
    Create Traceability matrix between RFLP components
  CATIA Functional & Logical Design
    Create and manage requirements, functional, and logical components
    Create Traceability matrix between RFLP components
    Note: In this course, we will primarily work with the Functional & Logical Design app.
Requirements
Functional & Logical Design

## Slide 7: Document Requirements

## Slide 8: Document Requirements
Documenting requirements helps to manage changes in products as per the customer requirements.
In addition to documenting customer requirements, the following tasks can be accomplished:
    Plan according to proposed requirements.
    Generate Traceability Reports related to requirements and their specifications.
    Configure requirements to reduce development costs and optimize project schedules.

## Slide 9: Scenario Walkthrough
Step 1
Promote Document Requirements task to In Work state.
Step 2
Import existing Survey Done Specification folder (named: Survey Drone).
Step 3
Create new requirement specification.
Step 4
Populate requirement specification with all needed requirements.
Step 5
Promote Document Requirements task to Complete state.

## Slide 10: Document Requirements

## Slide 11: Document Requirements
Click on the Task Menu icon for the Document Fuselage Requirements task.
Click Edit.
Modify the Maturity of the task and promote it to In Work.
Click Save.
1
2
4
3

## Slide 12: Document Requirements (Cont.)
Click My 3D Modeling Apps.
Select the Functional & Logical Design app.
5
6
    Note: The Systems Architecture Designer role is needed to access the Functional and Logical Design app.

## Slide 13: Document Requirements (Cont.)
In the RFLP tree, right-click on the Requirement node of the tree and select Insert  Insert Existing Specification Folder.
Search for [Survey Drone] in the Search Bar.
Select the Survey Drone specification folder that appears in the Search results window.
8
9
7

## Slide 14: Document Requirements (Cont.)
In the tree, right-click on the Survey Drone Specification Folder and select Insert  Insert New Requirement Specification.
In the Title field enter [Imaging].
Click OK.
10
12
11
Make sure “Set attributes at creation for all types” is set so that you can change the Title.

## Slide 15: Document Requirements (Cont.)
​‌Right-click on the Imaging requirement specification node and select Insert  Insert New Requirement.
13

## Slide 16: Document Requirements (Cont.)
In the Title field, enter [Stream Live Video].
Adjust the other parameters, as shown.
Click OK.
14
15
16

## Slide 17: Document Requirements (Cont.)
​‌Right-click on the Stream Live Video requirement node and select Insert  Insert New Parameter.
17

## Slide 18: Document Requirements (Cont.)
In the Title field, enter [Gigabytes]
Switch to the Select Parameter Type tab.
Set the Type field to Rate.
Set the Display Unit to Per second (_s) .
In the Value field type [1].
Click OK.
18
19
20
21
22
23